## Slide 1: Okumara and hata model
Wireless communication lab

## Slide 2: Okumura model
50th Percentile or median path loss is given as:
L50(db)=Lf + Amu(Fc,d)-G(hte)-G(hre)-Garea
L50(db) = the 50th percentile path loss in db
Lf = free space propagation loss
G(hte)=Transmit antenna height gain factor
G(hre)= Receive antenna height gain factor
Garea= Gain due to environment

## Slide 3
Free space loss (Lf) = (4*pi)^2 d^2/lambda^2
Lf(db)= 10log10((4*pi)^2*d^2/lambda^2)
G(hte)= 20log10(hte/200)
G(hre)=10log10(hre/3) ; hre< 3m
= 20log10(hre/3) ; 3m<hre<10m
Amu(Fc,d) is a correction factor as a function of carrier frequency Fc and distance d, these have been plotted for several values of Fc and d.
Garea is a correction factor for various environments has been computed (plotted) for different frequency.

## Slide 4: Example:
Calculate the mean path loss using Okumaras model for d=50 km, hte= 100 m, hre= 10 m and carrier frequency =900 MHz in a suburban environment. Write a MATLAB code for the model and also derive the useful result interpretation. Vary distance and height of the transmitter antenna and plot graph between
a) path loss and distance
b) path loss and height of the transmitter antenna.

## Slide 5: a) path loss and distance
hre =10;
F = 900*(10^6);
Lembda =(3*10^8))/f;
Garea = 9;
hte = 100;
D=(100*(10^3),90*(10^3), 80*(10^3), 70*(10^3), 60*(10^3), 50*(10^3), 40*(10^3), 30*(10^3), 20*(10^3), 10*(10^3));
Amu =(53 , 48 , 40 , 36 , 28 , 25 , 18 , 11 , 10 , 8);

## Slide 6: b) path loss and height
Hre = 10;
F= 900*(10^6);
Lambda = (3*(10^8))/f;
Garea =9;
D=50*(10^3);
Amu =40;
hte=(100,90,80,70,60,50,40,30,20,10);

## Slide 7: Urban area- hata model
Lu=69.55 + 26.16 log10(f) - 13.82 log10(hB) -
CH + (44.9 - 6.55 log10(hB)) log10d
Small and medium size city:
CH= 0.8 + (1.1 log10f - 0.7) hm - 1.56 log10f
large cities:
CH = 8.29 (log101.54hm)2 - 1.1 dB ; for f<=300 MHz
= 3.2 (log1011.75hm)2 - 4.97 dB ; for f>=300 MHz
Lu= path loss in urben areas in dB
hB= height of base station antenna in meter
hm=height of mobile station antenna in meter
f = frequency of transmitter in MHz
CH=antenna height correction factor
d =distance between base station and mobile station in km

## Slide 8: Suburban areas-hata model
Lsu = Lu - 2 (log10 (f/28))2 -5.4
Lsu=path loss in suburban areas in dB
Lu= average path loss in urban areas for small sized city in dB
Lu = 69.55+26.16log10(f)-13.82log10(hB)-CH +(44.9- 6.55log10(hB))log10d
CH = 3.2 (log1011.75hm)2 - 4.97 dB ; for f>=300 MHz
f= frequency of transmission in MHz

## Slide 9: Open area-hata model
Lo=Lu - 4.78 (log10f)2 + 18.33 log10f - 40.94
Lo=paht loss in open area in dB
Lu= path loss in urban area for small sized city in dB
Lu=69.55+26.16log10(f)-13.82log10(hB)-CH +(44.9- 6.55log10(hB))log10d
CH= 0.8 + (1.1 log10f - 0.7) hm - 1.56 log10f
f= frequency of transmission in MHz

## Slide 10: Example
Find the median path loss under the Hata model assuming fc = 900 MHz, transmitter antenna height = 40 m, receiver antenna height = 5 m and d = 20 km for a large urban city, a small urban city, a suburb, and a rural area. Explain qualitatively the path loss diﬀerences for these 4 environments. Also write MATLAB code for the model and derive the useful result interpretation. Compare the path loss obtained by this model with Okumara model in suburban area having same system speciﬁcations. Vary distance and plot graph between
1. Path loss and distance for all the four environments of Hata model
2. Path loss and distance for Okumura model
3. Path loss and distance for Okumura model
4. Compare the graphs obtained in diﬀerent model

## Slide 11
for distance variation:
f= 900MHz
hB=200
hm=3
d=(20,19,18,17,16,15,14,13,12,11,10) km
for transmitter height variation:
f= 900MHz
hB=(3,4,5,6,7)m
hm=5
D=10km